## Slide 1: Introduction to Sockets (part 1)
IP, ICMP, UDP, TCP header format, servers, byte ordering, socket file descriptors, POSIX data types and functions, useful tools
Chapters 1,2 and 3.

## Slide 2: IP Protocol Suite
Data Link
Network
Transport
Session
Presentation
Application
Ethernet/etc…
IP
TCP/UDP
Application
OSI
Reference Model
TCP/IP
Model
IPv4
IPv6
TCP
UDP
SCTP
mTCP
DCCP
RSVP
BGP, DHCP, DNS, FTP, HTTP, HTTPS,
IMAP, LDAP, MGCP, NNTP, NTP, POP
ONC/RPC, RTP, RTSP, RIP, SIP, SNMP, SMTP,
SSH, Telnet, TLS/SSL, XMPP,….
ICMP IGMP

## Slide 3: Internet Protocol
Two versions, v4 and v6.
  (Odd numbers are for research/testing, i.e. should not be seen in the wild) .
IPv4,
  Request for Comments (RFC) 791 (Sept. 1980).
  Internet Standard (STD) 5.
IPv6,
  RFC 8200 (…. July. 2017).
  Internet Standard
32-bit address space
Fragments
128-bit address space
No Fragments

## Slide 4: IP Principle
Unreliable and connectionless datagram delivery service.
Unreliable: No guarantees that a datagram will be successfully delivered to its destination.
IP provides Best Effort service.
Connectionless: IP will not maintain state information about successive datagrams. Each datagram is handled as an independent entity.

## Slide 7: Addressing
Version 4
  140.252.1.29
  194.47.151.182
Version 6
  2001:0db8:85a3:0000:0000:8a2e:0370:7334
  2001:db8:85a3:0:0:8a2e:370:7334
  2001:db8:85a3::8a2e:370:7334

## Slide 8: Version 6 – Simplified Notation
2001:0db8:85a3:0000:0000:8a2e:0370:7334
/0{1,4}/0/g -- /^0//g -- /0$//g --
2001:db8:85a3:0:0:8a2e:370:7334
/^0$//g -- /:{3,}/::/g
2001:db8:85a3::8a2e:370:7334

## Slide 9: Subnet Mask
Address + subnet mask => net ID & host id
  A & MASK => NetID
  A &!MASK => HostID
Two notations (examples)
  “Classbased” 255.255.255.0
  “Classless” /24

## Slide 10: Subnetting
Network Address
Host ID
Network Address
Host ID
Network Address
Host ID
Separate Network and Host parts

## Slide 11: Subnet Example: 192.168.0.1/26
Address: 192.168.0.1 11000000.10101000.00000000.00 000001
Netmask: 255.255.255.192 = 26 11111111.11111111.11111111.11 000000
Wildcard: 0.0.0.63 00000000.00000000.00000000.00 111111
Network: 192.168.0.0 11000000.10101000.00000000.00 000000
Broadcast: 192.168.0.63 11000000.10101000.00000000.00 111111
HostMin: 192.168.0.1 11000000.10101000.00000000.00 000001
HostMax: 192.168.0.62 11000000.10101000.00000000.00 111110
Hosts/Net: 62
Wildcard = !Netmask
Network = Address & Mask
Broadcast = Upper Network Address
Host Min = Network Address + 1
Host Max = Broadcast - 1

## Slide 12: Subnet Example: 194.47.151.65/25
Address: 194.47.151.65 11000010.00101111.10010111.0 1000001
Netmask: 255.255.255.128 = 25 11111111.11111111.11111111.1 0000000
Wildcard: 0.0.0.127 00000000.00000000.00000000.0 1111111
Network: 194.47.151.0 11000010.00101111.10010111.0 0000000
Broadcast: 194.47.151.127 11000010.00101111.10010111.0 1111111
HostMin: 194.47.151.1 11000010.00101111.10010111.0 0000001
HostMax: 194.47.151.126 11000010.00101111.10010111.0 1111110
Wildcard = !Netmask
Network = Address & Mask
Broadcast = Upper Network Address
Host Min = Network Address + 1
Host Max = Broadcast - 1

## Slide 13: Networks
192.168.0.0/24
Host
192.168.0.4
Host
192.168.0.5
Host
192.168.0.254
192.168.0.254
& 255.255.255.0
192.168.0.0
Grouping of Hosts
Simplifies Routing/Forwarding
192.168.0.4
& 255.255.255.0
192.168.0.0

## Slide 14: Networks
192.168.0.0/24
Host
192.168.0.4
Host
192.168.0.5
Host
192.168.0.254
192.168.1.30 & 255.255.255.0 = 192.168.1.0 != 192.168.0.0
192.168.1.0/24
Host
192.168.1.30
Router
192.168.0.x
192.168.1.y

## Slide 15: Networks
192.168.0.0/24
Host
192.168.0.4
Host
192.168.0.5
Host
192.168.0.254
192.168.1.0/24
Host
192.168.1.30
Router
192.168.0.x
192.168.1.y
192.168.2.0/24
Router
192.168.1.z
192.168.2.y
192.168.3.0/24
Router
192.168.1.x
Routing Table
192.168.0.0/24 local via 192.168.0.x
192.168.1.0/24 local via 192.168.1.y
192.168.3.0/24 remote via 192.168.1.x
192.168.2.0/24 remote via 192.168.1.z
Routing Table
192.168.2.0/24 local via 192.168.2.y
192.168.1.0/24 local via 192.168.1.z
192.168.3.0/24 remote via 192.168.1.x
192.168.0.0/24 remote via 192.168.1.y
Routing Table
192.168.3.0/24 local via 192.168.3.y
192.168.1.0/24 local via 192.168.1.x
192.168.0.0/24 remote via 192.168.1.y
192.168.2.0/24 remote via 192.168.1.z

## Slide 16: Internet -- Inter connection of Networks
192.168.0.0/24
192.168.1.0/24
Router
192.168.2.0/24
Router
192.168.3.0/24
Router
192.168.4.0/24
Router
192.168.5.0/24
Router
192.168.x.0/24
Router
192.168.x.0/24
Router
192.168.x.0/24
Router
192.168.x.0/24
Router
192.168.x.0/24
192.168.x.0/24
192.168.x.0/24
IP Router
Forwards IP datagrams
Minimum two Addresses on/in two different networks
Routing Table

## Slide 17: Subnet, Forwarding and Gateway
To: 8.8.8.8
192.168.1.12
192.168.1.0/24
Forwarding Table
Destination Gateway Genmask Flags Metric Ref Use Iface
0.0.0.0 192.168.1.1 0.0.0.0 UG 0 0 0 em1
192.168.1.0 0.0.0.0 255.255.255.0 U 0 0 0 br0
To: 192.168.1.14
192.168.1.14
192.168.1.14
& 255.255.255.0
192.168.1.0 <= NetID
Match!
Use!

## Slide 18: Subnet, Forwarding and Gateway
To: 8.8.8.8
192.168.1.12
192.168.1.0/24
192.168.1.1
8.8.8.8 & 255.255.255.0
Forwarding Table
Destination Gateway Genmask Flags Metric Ref Use Iface
0.0.0.0 192.168.1.1 0.0.0.0 UG 0 0 0 em1
192.168.1.0 0.0.0.0 255.255.255.0 U 0 0 0 br0
No Match!
= 8.8.8.0 <= NetID
8.8.8.8 & 0.0.0.0
= 0.0.0.0 <= NetID
Match!
Internet

## Slide 19: Intermediary Summary
IP v4 / v6
Networks / Subnetting
Forwarding / Routing

## Slide 20: Network to Data link
Data Link
Network
Ethernet
IP
OSI
Reference Model
TCP/IP
Model
Tokenring/bus
FDDI
…..

## Slide 21: Address Resolution Protocol (ARP)
Translate between Network and L2 address
10.1.0.59 ether b0:83:fe:bb:1d:8c C br0
10.1.0.53 ether 00:19:b9:12:79:32 C br0
194.47.151.112 ether d4:ae:52:ea:c9:30 C em1
194.47.151.65 ether 00:1b:53:99:53:ff C em1
10.1.0.62 ether 00:19:b9:20:c8:83 C br0
10.1.0.162 ether 54:9f:35:1f:c3:2a C br0
10.1.0.169 ether 08:00:27:30:ac:16 C br0
10.1.0.63 ether 00:19:b9:20:c7:48 C br0
10.1.0.42 ether 68:05:ca:24:45:36 C br0
194.47.151.126 ether 00:25:64:3b:cf:91 C em1

## Slide 22: Address Resolution Protocol (ARP)
Send to 10.1.0.42
10.1.0.59 ether b0:83:fe:bb:1d:8c C br0
10.1.0.53 ether 00:19:b9:12:79:32 C br0
194.47.151.112 ether d4:ae:52:ea:c9:30 C em1
194.47.151.65 ether 00:1b:53:99:53:ff C em1
10.1.0.62 ether 00:19:b9:20:c8:83 C br0
10.1.0.162 ether 54:9f:35:1f:c3:2a C br0
10.1.0.169 ether 08:00:27:30:ac:16 C br0
10.1.0.63 ether 00:19:b9:20:c7:48 C br0
10.1.0.42 ether 68:05:ca:24:45:36 C br0
194.47.151.126 ether 00:25:64:3b:cf:91 C em1
Eth.dst
68:05:ca:24:45:36
Eth.src
34:17:eb:ea:df:9f
IP.dst=10.1.0.42
0x0800

## Slide 23: Address Resolution Protocol (ARP)
Send to 10.1.0.46
10.1.0.59 ether b0:83:fe:bb:1d:8c C br0
10.1.0.53 ether 00:19:b9:12:79:32 C br0
194.47.151.112 ether d4:ae:52:ea:c9:30 C em1
194.47.151.65 ether 00:1b:53:99:53:ff C em1
10.1.0.62 ether 00:19:b9:20:c8:83 C br0
10.1.0.162 ether 54:9f:35:1f:c3:2a C br0
10.1.0.169 ether 08:00:27:30:ac:16 C br0
10.1.0.63 ether 00:19:b9:20:c7:48 C br0
10.1.0.42 ether 68:05:ca:24:45:36 C br0
194.47.151.126 ether 00:25:64:3b:cf:91 C em1
No match!

## Slide 24: ARP
Broadcast: Who has 10.1.0.46
Tell: 34:17:eb:ea:df:9f
…
10.1.0.42
10.1.0.17
10.1.0.48
10.1.0.52
10.1.0.46
68:05:ca:24:45:46

## Slide 25: ARP
To: 34:17:eb:ea:df:9f
10.1.0.46 is at
68:05:ca:24:45:46
…
10.1.0.42
10.1.0.17
10.1.0.48
10.1.0.52
10.1.0.46
68:05:ca:24:45:46

## Slide 26: Address Resolution Protocol (ARP)
Send to 10.1.0.46
10.1.0.59 ether b0:83:fe:bb:1d:8c C br0
10.1.0.53 ether 00:19:b9:12:79:32 C br0
194.47.151.112 ether d4:ae:52:ea:c9:30 C em1
194.47.151.65 ether 00:1b:53:99:53:ff C em1
10.1.0.62 ether 00:19:b9:20:c8:83 C br0
10.1.0.162 ether 54:9f:35:1f:c3:2a C br0
10.1.0.169 ether 08:00:27:30:ac:16 C br0
10.1.0.63 ether 00:19:b9:20:c7:48 C br0
10.1.0.42 ether 68:05:ca:24:45:36 C br0
194.47.151.126 ether 00:25:64:3b:cf:91 C em1
10.1.0.46 ether 68:05:ca:24:45:46 C br0

## Slide 27: Short overview of Transport Layer and Protocols

## Slide 28: Internet Main Transport Protocols
ICMP
UDP
TCP
….

## Slide 29: Internet Control Message Protocol

## Slide 30: User Datagram Protocol - UDP
Message Oriented Transport protocol
Unreliable Datagram Protocol
Can provide Integrity Verification (Checksum of header + payload)
Simple
Stateless

## Slide 32: Transmission Control Protocol
Reliable, ordered and error-checked delivery of a stream of octets (bytes).
End-to-end
Full-duplex

## Slide 33: TCP Protocol Operation
Connection Establishment
  Three way handshake
Data Transfer
Connection Termination

## Slide 34: TCP Protocol Operation
…
Connection Establishment
  Three way handshake
Data Transfer
  Full-duplex
Connection Termination
…
…
data
data
data
ack
ack
ack

## Slide 35: TCP Protocol Operation
Connection Establishment
  Three way handshake
Data Transfer
Connection Termination
  Three way handshake, in reverse.
  Single side-close
  s/SYN/FIN/

## Slide 36: TCP state transition diagram

## Slide 38: Summary
Overview of Networking
  Host
  Router
Layer 2 – 3 – Interaction
Overview of Transport protocols