## Slide 1: SSL/TLS and HTTPs
Secure Socket Layer, Transport Layer Security, Secure HTTP, Function Libraries for Encrypting Traffic
Online Material

## Slide 2: Security facilities in the TCP/IP stack
Pretty Good Privacy (PGP):
  a data encryption and decryption computer program
  provides cryptographic privacy and authentication for data communication.
  used for signing, encrypting and decrypting e-mails

## Slide 3
S/MIME (Secure/Multipurpose Internet Mail Extensions)
  a standard for public key encryption and signing of MIME data.
  provides the following cryptographic security services:
    authentication
    message integrity
    non-repudiation of origin (using digital signatures)
    privacy
    data security (using encryption)
Kerberos (the hound of Hades ):
  computer network authentication protocol
  allows nodes communicating over a non-secure network to prove their identity to one another in a secure manner.
  provides mutual authentication — both the user and the server verify each other's identity.
Security facilities in the TCP/IP stack

## Slide 4: SSL and TLS
SSL was originated by Netscape
TLS working group was formed within IETF
First version of TLS can be viewed as an SSLv3.1
SSL
  SSL Architecture
  SSL Record Protocol
  Change Cipher Spec Protocol
  Alert Protocol
  Handshake Protocol

## Slide 5: SSL architecture
Not a single protocol
  two layers of protocols
Provides basic security services to higher layer protocols
  e.g. HTTP operates on top of SSL
Three higher layer protocols are part of SSL

## Slide 6: SSL session / SSL connection
Two important concepts : SSL connection and SSL session
SSL connection
  Transport that provides a suitable type of service
  An SSL connection is peer-to-peer relationship (transient)
  Every SSL connection is associated with one session
SSL session
  Association between a client and a server
  Created by the Handshake Protocol
  Define a set of cryptographic security parameters
States :
  Session Established : Current operating state for receive and send
  Handshake Protocol: Pending State for receive and send
  If handshake successful, pending state becomes current operating state

## Slide 7: SSL record protocol: Services
Two services for SSL Connections
  Confidentiality
    Defines a shared secret key that is used for conventional encryption
  Message Integrity
    Defines a shared secret key that is used to form a message authentication code (MAC)
Compression
  Lossless compression to shrink the message size
  Default compression algorithm defined as NULL in SSLv3 and current version of TLS

## Slide 8: SSL record protocol: Operation
No distinction is made among various applications using SSL; the content of data is opaque to SSL
Fragment: 214 bytes
Compression: Optional
Message Authentication Code: shared secret key is used to compute MAC
Encryption: Symmetric

## Slide 9: SSL record protocol: Operation
First Step Fragmentation: Each upper layer message is fragmented into block of 214 bytes (16384 bytes) or less
Second Step Compression: Optional step, must be lossless and may not increase the length by more than 1024 bytes
Third Step Message Authentication Code (MAC): shared secret key is used to compute MAC
Fourth Step Encryption: compressed message (if applied) and MAC are encrypted using symmetric encryption
Final Step Header Preparation.

## Slide 10: SSL record format
Content Type (8 bits)
  Higher layer protocol used to process the enclosed fragment such as change_cipher_spec, alert, handshake and application data
Major Version (8 bits)
  Major Version of SSL e.g. For SSL v3 = 3
Minor Version (8 bits)
  Minor Version of SSL e.g. For SSL v3 = 0
Compressed Length (16 bits)
  The length in bytes of plaintext or compressed fragment

## Slide 11: SSL change cipher spec protocol
Uses SSL Record Protocol
Simplest one : Consists of a single message, which consists of single byte with value 1
Purpose is to convert pending state into current state

## Slide 12: Alert protocol
Conveys SSL-related alerts to peer
Compressed and Encrypted
Consists of two bytes
  The first byte indicates Alert Level (indicates severity)
    Warning
    Fatal
      Will immediately terminate the connection
      Alerts that always will be fatal
        unexpected_message, bad_record_mac, decompression_failure, handshake_failure, illegal_parameter
The second bytes indicates the specific alert
  Warning alerts
    close_notify, no_certificate, bad_certificate, unsupported_certificate, certificate_revoked, certificate_expired, certificate_unknown

## Slide 13: Handshake protocol
The most complex part of SSL.
Server and client authenticate each other.
Server and client negotiate encryption, MAC algorithm and cryptographic keys.
Used before any application data is transmitted.
Message Format
  Type: Indicate one of ten messages (e.g. Hello, certificate, key exchange)
  Length: The length of message
  Content: The parameters associated with this message

## Slide 14: Handshake protocol: Phases
Phase 1: Establish Security Capabilities
  Initiate logical connection and establish security capabilities to be associated with it.
Phase 2: Server Authentication and Key Exchange
  Sends a certificate (if authentication is required)
  May send Server_Key_Exchange message
Phase 3: Client Authentication and Key Exchange
  Client verifies certificate from server and server_hello parameters
  May send a certificate (on request) or alert for no certificate or one or more message
Phase 4: Finish
  Completes secure connection

## Slide 15: Handshake protocol in action

## Slide 16: Transport Layer Security (TLS)
The same record format as the SSL record format.
Defined in RFC 5246.
Similar to SSLv3.
Differences in the:
  version number : major version 3, minor version 3 (TLS v1.2)
  message authentication code (RFC 2104 HMAC)
  pseudo random function
  alert codes (same as SSLv3 except no_certificate)
  cipher suites : no longer support for Fortezza
  client certificate types
  certificate_verify and finished message
  cryptographic computations
  padding

## Slide 17: HTTPS
HTTP over SSL : combination of HTTP and SSL
  RFC 2818 : HTTP Over TLS , no fundamental change in HTTP over SSL or TLS
  Secure communication between Web browser and Web servers
  Built into all modern Web browser
  Web servers should support HTTPS communications
Connection Initiation
  Client initiates a connection to server on appropriate port (default: 443)
  SSL/TLS handshake is performed
  Data is sent
Connection Closure
  Client indicate closing of connection, Connection : close
  Client must be able to cope with a situation, if a connection is terminated without close notification and issue security warning

## Slide 18: APIs
Libcrypto
OpenSSL / LibreSSL
mbed TLS
Libcurl

## Slide 19: OpenSSL
Open Source toolkit implementing SSL v2/v3 and TLS protocols as well as a full-strength general-purpose cryptography library

## Slide 20: LibreSSL
LibreSSL is a version of the TLS/crypto stack forked from OpenSSL in 2014, with goals of modernizing the codebase, improving security, and applying best practice development processes.
More secure?

## Slide 21: mbed TLS
Former PolarSSL
Acquired by ARM and rebranded mbed TLS
Direct replacement for OpenSSL from a standard point of view
  Different API
Better documentation and code structure
More intuitive API
More secure?

## Slide 22: Libcurl
Highly portable and easy-to-use client-side URL transfer library
  Supports: DICT, FILE, FTP, FTPS, GOPHER, HTTP, HTTPS, IMAP, IMAPS, LDAP, LDAPS, POP3, POP3S, RTMP, RTSP, SCP, SFTP, SMTP, SMTPS, TELNET and TFTP.
  libcurl also supports HTTPS certificates, HTTP POST, HTTP PUT, FTP uploading, kerberos, HTTP form-based upload, proxies, cookies, user+password authentication, file transfer resume, http proxy tunneling and more!

## Slide 23: Client-server setup
Server
Client

## Slide 24: Server main()

## Slide 25: Client main()

## Slide 26: Common code

## Slide 27: Common code (cont.)

## Slide 28: Client tcp_connect()

## Slide 29: Server accept()

## Slide 30: Read/write
SSL_read(const SSL *ssl, void *buf, int num)
  Similar to read(), ssl is the SSL “file descriptor"
  Returns number of bytes read
SSL_write(SSL *ssl, const void *buf, int num)
  Similar to write(), ssl is the SSL “file descriptor”
  Returns number of bytes written
SSL_get_error(const SSL *ssl, int ret) should be used to test the return values (passed in ret)
  Returns SSL_ERROR_NONE if read/write was succesfull

## Slide 31: Terminate connection
SSL_shutdown(SSL *ssl) is used to shut down an active SSL/TLS connection
SSL_free() decrements the reference count of ssl
  If count reaches zero, the memory is freed
Don’t forget to close the socket as well!